## Slide 1: SO1-2 Trends in Land Productivity
Dr. Ingrid Teich
Senior Research Scientist (University of Bern)
WOCAT Secretariat

## Slide 2: METHODOLOGY
CONSTRUCTION PRODUCTIVITY TIME SERIES
GREEN INDEX DERIVED FROM REMOTE SENSORS
ANNUAL METRIC: mean

## Slide 3: LAND PRODUCTIVITY DYNAMICS
NEGATIVE TRENDS
Loss of Productivity
DEGRADATION
POSITIVE TRENDS
Increased Productivity
IMPROVEMENT

## Slide 4: PERIODS - LAND PRODUCTIVITY
16-years moving window

## Slide 5: DIFFERENT LPD MODELS
Trends.Earth
FAO WOCAT
PERIOD: BASELINE (2000-2015)
28%
17 %
JRC
4%

## Slide 6
https://docs.trends.earth/en/latest/for_users/downloads/index.html

## Slide 7: WHY SO MUCH DIFFERENCES IN THE RESULTS?
Because different data is used, it is analyzed in different ways, and each model can be parameterized, so even the same model and the same data can give different results.
THIS ALLOWS US TO FIND A MODEL ADJUSTED TO THE REALITY OF EACH COUNTRY, REGION, WORK AREA
LPD input data set + LPD algorithm

## Slide 8: For every pixel…
LPD ALGORITHM
LPD INPUT DATASET
LPD class: i.e. STABLE

## Slide 9: The LPD input data set

## Slide 10: The LPD input data set
Which vegetation index will be used as proxy for productivity
Which satellite imagery dataset will be used for the input data
How annual estimates will be calculated

## Slide 11: 1- Vegetation index
EVI: Enhanced vegetation Index
(corrects for atmospheric conditions and canopy background noise, more sensitive in areas with dense vegetation)
SAVI: Soil Adjusted Vegetation Index
(corrects the influence of soil brightness when vegetative cover is low
The LPD input data set

## Slide 12
2- Satellite imagery dataset
The LPD input data set

## Slide 13
3- Annual estimates
The LPD input data set

## Slide 14: For every pixel…
LPD ALGORITHM
LPD INPUT DATASET
LPD class: i.e. STABLE

## Slide 15: The LPD algorithm
JRC LPD
Trends.Earth LPD
FAO-WOCAT LPD
Default

## Slide 16
Annex: Default versions of globally available LPD maps
Co-authors:
Andreas Brink, Gabriel Daldegan, Cesar L. Garcia, Federico Gianoli, Ingrid Teich and Alex Zvoleff
Joint Research Centre default dataset
:
FAO-WOCAT LPD default dataset
FAO-WOCAT LPD default dataset

## Slide 17: Trends.Earth LPD
TRAJECTORY
STATE
PERFORMANCE
Measures the rate of change in primary productivity over time.
Compares the current productivity level in a given area to historical observations of productivity in that same area. ​
Measures local productivity relative to other similar vegetation types in similar land cover types or bioclimatic regions throughout the study area.

## Slide 18: Aggregation of metrics

## Slide 19: Distinguishing human induced land degradation from the effects of climate variability
WATER, LIGHT, TEMPERATURE
Different factors affect primary productivty
INTERPRETING VARIABILITY
Historical precipitation information as a context
CLIMATE CORRECTION METHODS
Residual Trend Analysis (RESTREND), Rain & Water Use Efficiency (RUE & WUE)

## Slide 20: RESIDUAL TREND ANALYSIS Trends in vegetation production independent of rainfall
Regression
between ΣNDVI and growth season sum ln(rainfall) per pixel.
RESIDUALS
Difference between observed and predicted ΣNDVI
Residuals Trend
RESTREND-residuals’ are regressed on time
1
2
3

## Slide 21: Turkistan Oblast, Kazakhstan
Trend
Restrend Chirps
Restrend Persiann
Restrend GPCP
RUE Chirps
WUE
RUE Persiann
RUE GPCP
2001-2018
2001-2018
2001-2018
2001-2018
2001-2018
2001-2018
2001-2018
2001-2018

## Slide 22: The LPD algorithm
JRC LPD
Trends.Earth LPD
FAO-WOCAT LPD

## Slide 23: The LPD algorithm
JRC LPD
Trends.Earth LPD
FAO-WOCAT LPD

## Slide 24: STRATEGY Use the “official” legend of 5 categories Produce a flexible approach were users can easily modify parameters Open code & FAIR data & easy access Base the development on the JRC simplified GEE code produced by FAO Integrate ideas implemented of Trends.Earth approach Co-development with countries and capacity building
Build on previous efforts and lessons learnt

## Slide 25: SCRIPT IN GEE
https://code.earthengine.google.com/?accept_repo=users/apacheta/LPD_FWversion2
New Version 2

## Slide 26: CATEGORIZATION:
03

## Slide 27: HIGH RESOLUTION FAO-WOCAT LPD
Two 30m input datasets:
1- HiLPD (https://www.nature.com/articles/s41597-025-04883-3 , https://doi.org/10.12237/casearth.686dc91f24e15709b381ae4e)

## Slide 28: HIGH RESOLUTION FAO-WOCAT LPD
Two 30m input datasets and LPD products:
2- ML30-LPD (https://doi.org/10.5281/zenodo.15276519)
García, C. L., Pozzi Tay, E. F., Raviolo, E., Maharaj, T., Francis, R., Zvoleff, A., Antunes Daldegan, G., Paredes-Trejo, F., Noon, M. & James, C (2025). Annual 30m NDVI Time Series from Mixed Landsat Images. Zenodo. https://doi.org/10.5281/zenodo.15276535

## Slide 29
Lon.: -71.59 Lat.: 19.64
ML30
HiLPD
FW 250m
Different input datasets
Same LPD algorithm

## Slide 30
30m NDVI Time Series for SIDS
García, C. L., Pozzi Tay, E. F., Raviolo, E., Maharaj, T., Francis, R., Zvoleff, A., Antunes Daldegan, G., Paredes-Trejo, F., Noon, M. & James, C (2025). Annual 30m NDVI Time Series from Mixed Landsat Images. Zenodo. https://doi.org/10.5281/zenodo.15276535
Li, X., Shen, T., Chen, Y., Chen, J., & Yang, Z. (2025). 30m NDVI dataset of Small Island Developing States from 2000 to 2023. Zenodo. https://doi.org/10.5281/zenodo.15862965
LPD ready to use at 30m for SIDS
García, C. L., Raviolo, E., Francis, R., Maharaj, T., Zvoleff, A., Antunes Daldegan, G.,Pozzi Tay, E. F., Paredes-Trejo, F., Noon, M. & James, C. (2025). A 30m Land Productivity Dynamic Dataset for SIDS computed from Mixed Landsat Time Series and FWv2 model [Data set]. Zenodo. https://doi.org/10.5281/zenodo.15276519
Xiaosong Li & Tong Shen. Land Productivity Dynamics Product of Small Island Developing States (30 meters Resolution), International Research Center of Big Data for Sustainable Development Goals (CBAS). Big Earth Data Center, CAS, 2025. DOI: https://doi.org/10.12237/casearth.686dc91f24e15709b381ae4e
Codes for other interested countries
Mixed Landsat: https://code.earthengine.google.com/?accept_repo=users/apacheta/Mixed_Landsat_NDVI_TS_National
HiLPD: https://github.com/ShenTong53/30m-annual-NDVI-calculation-from-2000-to-2023
HR LDP Data for SIDS and overflow to the world…

## Slide 31
3.2 Enhancements for Assessing Trends in Land Productivity
3.2.3 Verifying results and selecting the most representative LPD dataset

## Slide 32
3.2 Enhancements for Assessing Trends in Land Productivity
3.2.4 Workflow for selecting the most representative LPD map
Step 1: Establishing a Multidisciplinary Group of Experts
Step 2: Training and Capacity Building
Step 3: Determining the Need for a Subnational Analysis
Step 4: Exploring Alternative LPD Datasets
Step 5: Identifying Verification Data and Expert Knowledge
Step 6: Comparing the Performance of Alternative LPD Maps
Step 7: Selecting the Most Representative LPD Map

## Slide 33: BHUTAN - 2022
AVAILABLE LAYERS TO USE IN 2026
Districts
Mines
Landslides-LD sites
Basins
AEZ

## Slide 34: Is field verification possible?
Silvopastoral system since 2020, combining tree cover with livestock grazing.
Eucalyptus, planted in different spatial arrangements, including concentric patterns, which help optimize both shade distribution and grazing space.
Before 2020 it was used as pastureland for livestock production.

## Slide 35: Thank you
Do you have any questions?
Ingrid.teich@unibe.ch