## Slide 1: SO1-1 Trends in Land Cover
Dr. Ingrid Teich
Senior Research Scientist (University of Bern)
WOCAT Secretariat
Cambodia
July 2nd 2026

## Slide 2: SDG 15.3.1 PROPORTION OF LAND THAT IS DEGRADED
TRENDS IN LAND COVER
TRENDS IN LAND PRODUCTIVITY
TRENDS IN CARBON STOCKS
“While it is difficult for a single indicator to fully capture the state or condition of the land, the sub-indicators are proxies to monitor the essential variables that reflect the capacity of the land to deliver ecosystem services” Sims et al. 2021
SO1-1
SO1-2
SO1-3
“transformational” variable
“fast” ecological variable
“slow” ecological variable
Notes: By establishing and implementing relevant SLM measures, it is expected that land degradation will be avoided, reduced, or reversed (according to the UNCCD response hierarchy), enabling progress towards a land degradation neutral world (SDG 15.3). Accordingly, it is expected that these changes will eventually impact on the proportion of land that is degraded over total land area (SDG indicator 15.3.1). To assess this indicator, the Good Practice Guidance (GPG, Sims et al. 2019; Sims et al., 2021), developed by the UNCCD, recommends the calculation of three Change of State indicators: (1) Trends in land cover, (2) Trend in land productivity or functioning of the land and (3) trends in carbon stocks above and below ground. Regional and global datasets derived from global earth observation systems play an important role to obtain these indicators, particularly for assessing changes in land productivity and land cover dynamics
The results of the degradation analysis for each of the sub-indicators are integrated using a one out- all-out (1OAO) method in which a significant reduction or negative change in any one of the three sub-indicators is considered to comprise land degradation. The GPG provides details on how to calculate the extent of land degradation for reporting on SDG Indicator 15.3.1 according to the Tier I methods adopted by the UN Statistical Commission.
It is important to notice that it is difficult for a single indicator to fully capture the state or condition of the land. The sub-indicators are proxies to monitor the essential variables that reflect the capacity of the land to deliver ecosystem services, but additional sub-indicators may be required to fully assess land degradation in some areas and under certain conditions.
More information:
https://www.unccd.int/sites/default/files/documents/2021-09/UNCCD_GPG_SDG-Indicator-15.3.1_version2_2021.pdf
Teich, I., Gonzalez Roglich, M., Corso, M.L. and García, C.L. 2019. Combining Earth Observations, Cloud Computing, and Expert Knowledge to Inform National Level Degradation Assessments in Support of the 2030 Development Agenda. Remote Sens., 11: 2918.

## Slide 3: METHODOLOGY
INITIAL LAND COVER
DEGRADATION DUE TO LAND COVER CHANGE
GAINS
TRANSITIONS / CHANGES
FINAL LAND COVER
TRANSITION MATRIX
LOSSES

## Slide 4
LAND COVER - PERIODS
Years: 2000, 2015, 2019, 2023
4 Land Cover Maps

## Slide 5: STEP 1: Identification of the best available land cover dataset
https://doi.org/10.3389/frsen.2022.856903
https://maps.elie.ucl.ac.be/CCI/viewer/download/ESACCI-LC-Ph2-PUGv2_2.0.pdf
DEFAULT DATASET
ALTERNATIVE HIGH-RESOLUTION DATASETS
https://doi.org/10.5194/essd-13-2753-2021
ESA (European Space Agency)
CCI 300 m
annually 2000-2022
GLAD (University of Maryland)
GLAD GLC 30 m
2000, 2005, 2010, 2015, 2020
CBAS (SDG Center, China)
GLC-FCS30D - 30 m
annually 2000-2022

## Slide 6
3.1 Enhancements for Assessing Trends in Land Cover
3.1.1 Identification of the best available land cover dataset

## Slide 7: STEP 1: DATA SOURCE
Is it worth it to look for alternative land cover datasets or is the default data good enough?
What other datasets are available?
Is there a national data option that could be used? Or that can be used for improving or validating alternatives options?

## Slide 8
STEP 2: Selecting a land cover legend for monitoring key degradation processes
DEFAULT
ALTERNATIVES

## Slide 9
DEFAULT DATA can be recategorized
ESA reclass in 2022

## Slide 10: STEP 2: CATEGORIZATION
What are the main land use/cover changes related to degradation and restoration processes?
Is the 7-category legend sufficient to monitor these processes?
What other land classes would be important to monitor?

## Slide 11: STEP 3: Defining the land cover transition matrix
KEY: Participatory Decision-Making Process

## Slide 12
3.1 Enhancements for Assessing Trends in Land Cover
3.1.3 Defining the land cover transition matrix

## Slide 13
STEP 3: Defining the land cover transition matrix

## Slide 14
In many cases, differences in the interpretation of the same type of land cover transition arise from varying local contexts. A transition that signifies improvement in one area may represent degradation in another, depending on environmental, social, or economic conditions. Some countries are addressing this challenge by adopting a subnational approach to LDN monitoring and SDG Indicator 15.3.1 estimation. This approach acknowledges that a one-size-fits-all transition matrix is not always appropriate, particularly in countries with diverse bioclimatic conditions.
STEP 3: Defining the land cover transition matrix

## Slide 15
REGIÓN ORIENTAL
REGIÓN OCCIDENTAL
STEP 3: Defining the land cover transition matrix
REGIÓN ORIENTAL
REGIÓN OCCIDENTAL

## Slide 16: STEP 3: TRANSITION MATRIX
Does the default transition matrix represent the country?
Would it be advisable to have different matrices for different regions?
Which stakeholders should participate in this discussion?

## Slide 17: How can countries make these decisions?
FAO WOCAT PARTICIPATORY APPROACH FOR ESTIMATING SDG 15.3.1 FAO WOCAT LCT Apps

## Slide 18: Cambodia Land Cover Comparison App
https://wocatapps.projects.earthengine.app/view/compare-lct-khm

## Slide 19: Who makes the decisions?
INITIAL LAND COVER
DEGRADATION DUE TO LAND COVER CHANGE
GAINS
TRANSITIONS / CHANGES
FINAL LAND COVER
TRANSITION MATRIX
LOSSES

## Slide 20: Default data in PRAIS 4

## Slide 21: Lets explore the App
https://wocatapps.projects.earthengine.app/view/compare-lct-khm

## Slide 22: Hands on!
Which proportion of Cambodia was degraded between 2000 and 2015 according to the default data at national level?
How many ha of croplands were converted to tree covered areas between 2000 and 2015 according to the default data set?
https://wocatapps.projects.earthengine.app/view/compare-lct-khm

## Slide 23: Thank you
Do you have any questions?
Ingrid.teich@unibe.ch